TSIU03
REQUIREMENT SPECIFICATION

Project group: Date:

Priority 1 means that you must implement it. Priority 2 requirements are less important, but you must implement some of them. Priority 3 requirements will only be implemented if there is time left at the end of the project.

1) Basic Requirements
Req. #	Requirement	Priority
1	The system shall process an audio signal digitally.	1
2	The audio signal is read from, and sent back to the WM8731 chip.	1
3	The system shall display all settings on a VGA screen.	1
4	The user shall be able to control all settings from a PS/2 keyboard.	1
5a	The system shall have a volume control with at least 10 levels.	1
5b	The volume control shall span at least 27 dB between lowest and highest level.	1
5c	The difference between levels shall be constant (in logaritmic scale).	1
5d	The system shall implement a mute function.	1
6a	The system shall have a balance control with at least 10 levels.	1

2) Subproject 1: Digital Oscilloscope
Req. #	Requirement	Priority
7	The system shall display a picture of the current sound wave form.	1
8	Each frame of the VGA screen shows exactly one recording of the sound. / (this means that the recording must not change while it is displayed).	1
9	Each recording must be synchronized to a positive zero-transition of the sound signal. / (this is to reduce the flickering. A pure sinusoid will then appear stable).	2
10
11

More possibilities: Zoom in time and/or amplitude, show stereo signal, autodetect under/overflow.

2) Subproject 2: Signal Level Indicator
Req. #	Requirement	Priority
7	The system shall display the output sound power level on the screen.	1
8a	The power of each output channel shall be displayed as a bar.	1
8b	The scale of the bars shall be logarithmic.	1
8c	The displayed power is low pass filtered, so it contains information from all sound samples at least 100 ms back in time.	1
9a	Each bar has a peak level indicator.	2
9b	The peak level indicator must never show less level than the bar.	2
9c	The peak level indicator falls slowly when the power bar is lower than the peak level indicator.	2
10

More possibilities: Changeable low pass filter settings. Different behavior of the peak level indicator. Showing input power level as well (before the volume control).

2) Subproject 3: Echo
Req. #	Requirement	Priority
7	The system shall produce an echo of the signal.	1
8a	The user shall be able to set the delay of the echo.	1
8b	The maximum delay of the echo must be at least 1 s.	1
9a	The system shall have a volume control of the echo.	1
9b	The user shall be able to set the volume of the echo.	1
10

More possibilities: Mono vs. Stereo, toggle left/right channel in the echo, echo of input or output (the later gives echo-on-echo effects).

2) Subproject 4: Equalizer
Requirement: It is recommended that the students have taken a course in digital filters in order to do this task.
Req. #	Requirement	Priority
7	The system shall have a mono function that calculates the average of left and right channel.	1
8	The system shall have an equalizer that splits the audio signal into two frequency bands.	1
9	The lower frequency band shall be sent to the output left channel, the higher band to the output right channel.	1
10	The user shall be able to amplify the lower and higher bands individually.	2
11	The user shall be able to set the mono+equalizer on or off. When off, the sound is just bypassed.	1
12	The volume and balance feature (Req. #5 and #6) must be applied after the equalizar.	2
13
14

More possibilities: More bands, then it must be defined which bands are going to which speaker.

3) Distinctive features: What makes your system unique.
Requirement: You must convince the supervisor that you will be able to implement what you suggests here.
Req. #	Requirement	Priority

Possibilities: Background images, gradients here and there, fancy animations, play piano on the keyboard, pitching the sound, mute, toggle this or that, use the LCD, "blue screen" when too loud music, laser show, voice control, skynet etc.